Differential Doppler RDF
Another crazy HAM idea from W2VX

---
Objective
- Radio direction finder implementation
  - Use an N antenna circular array with rotating selective switching to produce a Doppler tone from a fixed reference(Tr) and unknow transmitter(Tu).
    - The demodulated phase difference between Tr and Tu will be used to estimate a direction (D and D+180deg) to Tu
    - Changing the orientation of Tr with respect to Tu will be used to rate D or D+ as the most likely direction vector to Tu.
    - Advantages - ? Accuracy, mobility, ease of use. Reasonable cost.
    - Disadvantages – depends on what existing systems approaches are being compared.

---
Concept
Circular
Doppler
N array
(Tr)
Compute engine with
GnuRadio Companion
And Python sigLib
Antenna
 N Coax
(Tu)
FFT
Spectral
Location
Direction
Orientation
Doppler
Antenna
Controller
Tuner
Web Service
Demodulate
Tr
Bandpass
Tr
Combined
Modulated
Doppler
Signals
Demodulate
Tu
Bandpass
Tu
Tu - Tr
2 RTL
Coherent receivers
Tuned to Tr and Tu
Respectively
USB
FFT
Spectral
Visualizer
Tuner
Tu